## Slide 1: 1. PV-30 capsules: stability review
Parvessune Pharmaceuticals | WA/2021/270 | 03 Oct 2022
Notes: Final readout. Protocol opened 30 Sep 2021; approved results completed 30 Sep 2022. LIMS accession WST-21-008374. An impurity reference resolved a late-eluting peak. Parvessune retained the capsule formulation for transfer.

## Slide 2: 2. Approved numerical evidence
Condition | Timepoint (months) | Assay (% LC) | Total impurities (%) | Result
25 °C/60% RH | 0 | 100.2 | 0.17 | Complies
25 °C/60% RH | 1 | 99.8 | 0.23 | Complies
25 °C/60% RH | 3 | 100.1 | 0.23 | Complies
25 °C/60% RH | 6 | 99.7 | 0.25 | Complies
25 °C/60% RH | 9 | 100.6 | 0.27 | Complies
25 °C/60% RH | 12 | 100.0 | 0.28 | Complies
30 °C/65% RH | 0 | 100.2 | 0.17 | Complies
30 °C/65% RH | 1 | 100.2 | 0.15 | Complies
30 °C/65% RH | 3 | 100.1 | 0.23 | Complies
30 °C/65% RH | 6 | 99.7 | 0.32 | Complies
30 °C/65% RH | 9 | 99.4 | 0.38 | Complies
30 °C/65% RH | 12 | 99.2 | 0.46 | Complies
40 °C/75% RH | 0 | 100.2 | 0.17 | Complies
40 °C/75% RH | 1 | 99.6 | 0.23 | Complies
40 °C/75% RH | 3 | 99.3 | 0.42 | Complies
40 °C/75% RH | 6 | 99.2 | 0.66 | Complies
Westravelle Analytical Ltd, a Tarnovell company | Confidential 2
Notes: Source: E-007 / PV30_PULLS_AND_SUITABILITY_RESULTS_Rev03.xlsx, approved 30 Sep 2022. Assay is percent label claim; total impurities are area percent. Condition and pull interval remain part of each result identity. Individual impurities and water results are retained in the full sequence sheets.

## Slide 3: 3. Protocol identity and sample custody
Client: Parvessune Pharmaceuticals
Protocol: WA/2021/270 | LIMS: WST-21-008374
Opened 30 Sep 2021; completed 30 Sep 2022
Dr L. Wu: stability lot and sample-custody reconciliation.
Storage condition and pull interval are carried with the stability lot on the batch card.
Sequence sheets retain the pack or presentation identity; results must not be pooled across storage conditions.
Tested interval: through 12 months.
Westravelle Analytical Ltd, a Tarnovell company | Confidential 3
Notes: The accession links receipt, batch card, preparation and analytical sequence. This readout does not introduce new lot codes or replace approved sequence sheets.

## Slide 4: 4. HPLC method qualification
Parameter | Result | Acceptance
Linearity (r²) | 0.9993 | ≥0.999
Range (% nominal) | 50-150 | 80-120 minimum
Accuracy 80% (% recovery) | 99.2 | 98.0-102.0
Accuracy 100% (% recovery) | 100.1 | 98.0-102.0
Accuracy 120% (% recovery) | 100.6 | 98.0-102.0
Repeatability (%RSD, n=6) | 0.34 | ≤2.0
Intermediate precision (%RSD) | 1.22 | ≤2.0
LOQ (% of nominal) | 0.05 | ≤0.05
Westravelle Analytical Ltd, a Tarnovell company | Confidential 4
Notes: Saira Mahmood, QC Method Validation Lead: qualification review. Read each result against its stated acceptance criterion. Assay and related-substances validation supports the reported sample preparation and separation; extensions require a separately agreed protocol.

## Slide 5: 5. Impurity trend by storage interval
Westravelle Analytical Ltd, a Tarnovell company | Confidential 5
Notes: An impurity reference resolved a late-eluting peak. The plot is a view of the approved stability table; the table supplies condition, interval and compliance status. Do not extrapolate beyond 12 months.

## Slide 6: 6. System suitability and deviation disposition
Saira Mahmood: analytical method and system suitability review.
Dr L. Wu: reconciliation of preparation, storage and sequence identity.
Dr A. Penrose: approved interpretation and client release.
Approved sequence sheets are the authority for suitability acceptance and any repeat sequence.
Deviation notes remain linked to the affected batch card; this deck does not replace their disposition.
No additional chamber excursion, reinjection or acceptance limit is inferred from the trend plot.
Westravelle Analytical Ltd, a Tarnovell company | Confidential 6
Notes: Readout source: PV30_PULLS_AND_SUITABILITY_RESULTS_Rev03.xlsx. Distinguish an observed formulation or packaging effect from an analytical deviation. An impurity reference resolved a late-eluting peak.

## Slide 7: 7. Interpretation for transfer
An impurity reference resolved a late-eluting peak.
Parvessune retained the capsule formulation for transfer.
Transfer the capsule formulation with the impurity reference and peak-assignment instructions.
Conclusion applies to tested storage conditions and the reported 12-month interval.
Westravelle Analytical Ltd, a Tarnovell company | Confidential 7
Notes: The impurity reference settled the late-eluting peak interpretation. Retention alone is not a general identity claim for unrelated peaks.

## Slide 8: 8. Release gate and client decision
Parvessune retained the capsule formulation for transfer.
Release basis: PV30_PULLS_AND_SUITABILITY_RESULTS_Rev03.xlsx; approved 30 Sep 2022.
Transfer the capsule formulation with the impurity reference and peak-assignment instructions.
Archive the approved readout with the sequence sheets, batch cards and linked deviation notes.
Westravelle Analytical Ltd, a Tarnovell company | Confidential 8
Notes: Dr A. Penrose | Head of Analytical Services | 03 Oct 2022. Final client readout for Parvessune Pharmaceuticals. Later shelf-life conclusions require additional approved pulls.