## Slide 1: 1. WX-4 tablets: stability review
Wexanthel Medicines | WA/2015/137 | 26 Jan 2017
Notes: Final readout. Protocol opened 22 Jul 2015; approved results completed 23 Jan 2017. LIMS accession WST-15-004255. The qualified method detected a packaging-dependent impurity trend. Wexanthel adopted the higher-barrier blister.

## Slide 2: 2. Approved numerical evidence
Condition | Timepoint (months) | Assay (% LC) | Total impurities (%) | Result
25 °C/60% RH | 0 | 100.4 | 0.20 | Complies
25 °C/60% RH | 1 | 100.1 | 0.23 | Complies
25 °C/60% RH | 3 | 100.3 | 0.22 | Complies
25 °C/60% RH | 6 | 100.7 | 0.31 | Complies
25 °C/60% RH | 9 | 100.2 | 0.24 | Complies
25 °C/60% RH | 12 | 100.5 | 0.35 | Complies
25 °C/60% RH | 18 | 100.1 | 0.41 | Complies
30 °C/65% RH | 0 | 99.9 | 0.18 | Complies
30 °C/65% RH | 1 | 100.5 | 0.24 | Complies
30 °C/65% RH | 3 | 100.4 | 0.25 | Complies
30 °C/65% RH | 6 | 99.9 | 0.37 | Complies
30 °C/65% RH | 9 | 99.1 | 0.35 | Complies
30 °C/65% RH | 12 | 99.9 | 0.47 | Complies
30 °C/65% RH | 18 | 99.0 | 0.55 | Complies
40 °C/75% RH | 0 | 100.6 | 0.16 | Complies
40 °C/75% RH | 1 | 100.7 | 0.27 | Complies
Westravelle Analytical Ltd | Confidential 2
Notes: Source: E-004 / WX4_PULLS_AND_SUITABILITY_RESULTS_Rev03.xlsx, approved 23 Jan 2017. Assay is percent label claim; total impurities are area percent. Condition and pull interval remain part of each result identity. Individual impurities and water results are retained in the full sequence sheets.

## Slide 3: 3. Protocol identity and sample custody
Client: Wexanthel Medicines
Protocol: WA/2015/137 | LIMS: WST-15-004255
Opened 22 Jul 2015; completed 23 Jan 2017
Dr L. Wu: stability lot and sample-custody reconciliation.
Storage condition and pull interval are carried with the stability lot on the batch card.
Sequence sheets retain the pack or presentation identity; results must not be pooled across storage conditions.
Tested interval: through 18 months.
Westravelle Analytical Ltd | Confidential 3
Notes: The accession links receipt, batch card, preparation and analytical sequence. This readout does not introduce new lot codes or replace approved sequence sheets.

## Slide 4: 4. HPLC method qualification
Parameter | Result | Acceptance
Linearity (r²) | 0.9997 | ≥0.999
Range (% nominal) | 50-150 | 80-120 minimum
Accuracy 80% (% recovery) | 99.7 | 98.0-102.0
Accuracy 100% (% recovery) | 99.8 | 98.0-102.0
Accuracy 120% (% recovery) | 99.7 | 98.0-102.0
Repeatability (%RSD, n=6) | 0.31 | ≤2.0
Intermediate precision (%RSD) | 1.17 | ≤2.0
LOQ (% of nominal) | 0.03 | ≤0.05
Westravelle Analytical Ltd | Confidential 4
Notes: Saira Mahmood, QC Method Validation Lead: qualification review. Read each result against its stated acceptance criterion. Assay and related-substances validation supports the reported sample preparation and separation; extensions require a separately agreed protocol.

## Slide 5: 5. Impurity trend by storage interval
Westravelle Analytical Ltd | Confidential 5
Notes: The qualified method detected a packaging-dependent impurity trend. The plot is a view of the approved stability table; the table supplies condition, interval and compliance status. Do not extrapolate beyond 18 months.

## Slide 6: 6. System suitability and deviation disposition
Saira Mahmood: analytical method and system suitability review.
Dr L. Wu: reconciliation of preparation, storage and sequence identity.
Dr A. Penrose: approved interpretation and client release.
Approved sequence sheets are the authority for suitability acceptance and any repeat sequence.
Deviation notes remain linked to the affected batch card; this deck does not replace their disposition.
No additional chamber excursion, reinjection or acceptance limit is inferred from the trend plot.
Westravelle Analytical Ltd | Confidential 6
Notes: Readout source: WX4_PULLS_AND_SUITABILITY_RESULTS_Rev03.xlsx. Distinguish an observed formulation or packaging effect from an analytical deviation. The qualified method detected a packaging-dependent impurity trend.

## Slide 7: 7. Interpretation for transfer
The qualified method detected a packaging-dependent impurity trend.
Wexanthel adopted the higher-barrier blister.
Carry the higher-barrier blister into transfer; keep the packaging comparison attached to the stability lot history.
Conclusion applies to tested storage conditions and the reported 18-month interval.
Westravelle Analytical Ltd | Confidential 7
Notes: The packaging decision follows the impurity trend detected by the qualified method. Do not recast that trend as a generic analytical failure.

## Slide 8: 8. Release gate and client decision
Wexanthel adopted the higher-barrier blister.
Release basis: WX4_PULLS_AND_SUITABILITY_RESULTS_Rev03.xlsx; approved 23 Jan 2017.
Carry the higher-barrier blister into transfer; keep the packaging comparison attached to the stability lot history.
Archive the approved readout with the sequence sheets, batch cards and linked deviation notes.
Westravelle Analytical Ltd | Confidential 8
Notes: Dr A. Penrose | Head of Analytical Services | 26 Jan 2017. Final client readout for Wexanthel Medicines. Later shelf-life conclusions require additional approved pulls.