## Slide 1: Clearance normalisation: microsomal vs hepatocyte CLint
Internal DMPK working deck | v2 | 03/17/2014
Notes: v2 of the Friday version. Still need to fix the mg/ml vs mg/mL labels before this goes to Megan.

## Slide 2: Why this deck
Microsomal and hepatocyte CLint are being reported side by side on the same test article sets, and the units do not line up
Need one agreed normalisation before the exposure gate memo goes out
  Current memo draft uses µL/min/mg for both assays; that is not right for the hepatocyte data
Species assumptions still differ between the two worksheets
Merrivoss Bioanalysis Inc | Confidential 2
Notes: Megan asked for a one-pager on this. This is the long version, cut it down later.

## Slide 3: How each assay is normalised
Parameter | Microsomal CLint | Hepatocyte depletion CLint
Matrix | Liver microsomes, pooled | Cryopreserved hepatocytes, single lot per species
Scaling basis | Microsomal protein (mg/mL in incubation) | Viable cells (10^6 cells/mL in incubation)
Reported unit | µL/min/mg | µL/min/10^6 cells
Species run | Rat, mouse, human | Rat and human; mouse on request
Interpretation | Intrinsic clearance, enzyme-only | Intrinsic clearance including uptake and phase II
Merrivoss Bioanalysis Inc | Confidential 3
Notes: The mg/ml vs mg/mL spelling is inconsistent across the worksheets. Pick one and stick to it.

## Slide 4: Unit conversion: the trap
Protein-normalised and cell-normalised values are not interchangeable
  A direct comparison needs the scaling step written out in the methods, not assumed
Some legacy worksheets carry µM and nM labels on the same column
  Check the concentration unit on each worksheet before merging
Clearance is reported only where the depletion curve is log-linear over the sampling window
Merrivoss Bioanalysis Inc | Confidential 4

## Slide 5: Species assumptions
What we are assuming and what we have not checked
Merrivoss Bioanalysis Inc | Confidential 1

## Slide 6: Species: what we have and what we assume
Rat and human microsomes run on every test article set
Mouse microsomes only for compounds going into rodent PK
Hepatocyte lots are single-donor per species, so donor variability is not averaged out
Assumed: rat clearance tracks human closely enough to rank compounds
Not checked: whether mouse hepatocytes behave like mouse microsomes
[TBC] human hepatocyte lot for Q2 still awaiting matrix acceptance
Merrivoss Bioanalysis Inc | Confidential 6
Notes: Carole has the donor sheets. Ask her before we say anything about mouse.

## Slide 7: Matrix acceptance for the two assays
Microsomal runs: matrix acceptance uses the positive control set and the no-cofactor control
Hepatocyte runs: viability is checked before dosing and again at the final time point
A run is only used if both controls fall inside their historical windows
  Failed runs are repeated, not interpolated
Merrivoss Bioanalysis Inc | Confidential 7
Notes: Helen wants the acceptance wording copied exactly from the SOP, not paraphrased.

## Slide 8: Analyte cards and quantitation
Each analyte card records the calibration range used for the depletion measurement
Tandem-MS quantitation on the parent-to-product transition, internal standard on every sample
Depletion half-lives derived only from points inside the calibration range
Merrivoss Bioanalysis Inc | Confidential 8

## Slide 9: What goes into the exposure gate
Microsomal CLint, species-matched to the PK study
Hepatocyte CLint where phase II contribution is suspected
Units stated in every table header
Assumptions footnoted, not buried in the methods
Merrivoss Bioanalysis Inc | Confidential 9

## Slide 10: Open points
Agree one unit convention for protein and cell basis across both worksheets
Confirm mouse hepatocyte value is needed for any current study
Decide whether the exposure memo quotes both CLint values or only the protein-normalised one
Clean up the legacy worksheet labels before archiving
Merrivoss Bioanalysis Inc | Confidential 10
Notes: Don't send this version outside the department. The v3 will have the agreed units.

## Slide 11: Next steps
Megan to review the normalisation table this week
Javier to confirm the mass-spec transitions used for the hepatocyte samples
Anna to pull the donor sheets for the human hepatocyte lot
Revise deck to v3 once units are agreed
Merrivoss Bioanalysis Inc | Confidential 11

## Slide 12: Back-up: reference compounds
Verapamil and ketoconazole used as reference compounds for both assays
Reference values checked at the start of each run against the lab's historical window
Generic reagent lots recorded on the assay worksheet
Merrivoss Bioanalysis Inc | Confidential 12
Notes: Left this in from the old version. Probably delete before v3.