## Slide 1: Plate acceptance for primary potency screens
Brindlewythe Biosciences Ltd | Biology training, v2
Notes: Second version after the September review. v1 is in the Training folder; use this one for the new starters.

## Slide 2: Why plate acceptance comes first
A plate is accepted before any compound on it is read for potency
Accepting a plate means the controls behaved as the protocol expects
  Acceptance is recorded on the run sheet, not in the bench notebook
A failed plate is rerun or excluded; it is never averaged into the set
Brindlewythe Biosciences Ltd | Confidential 2

## Slide 3: Controls on every plate
Positive control: reference kinase inhibitor at full response, duplicate wells across the plate
Negative control: vehicle only, same DMSO as the test wells
  Keep the DMSO percentage identical across the plate
Reference compound run as a dose response on each plate
  Staurosporine is the house reference for this assay
Brindlewythe Biosciences Ltd | Confidential 3
Notes: AV: is the reference titration still on every plate or only on the first plate of a set? Check before the next round.

## Slide 4: Control drift across a screening set
Plot the positive and negative control signal against plate order
A slow drift across the set is a reagent or temperature question
  Look at the incubator log before reading the compounds
A step change between two plates usually means a new reagent lot
  Record the test lot number on the run sheet
Drift alone does not fail a plate if both controls still sit inside the window
Brindlewythe Biosciences Ltd | Confidential 4
Notes: MS: the drift chart template is on the shared drive under Biology. The old copy in my folder is out of date.

## Slide 5: Accept or rerun
Accept when both controls are inside the window
Accept when the reference dose response falls on its curve
Accept with a note when one duplicate well is flagged and the rest agree
Rerun when a control is outside the window
Rerun when the edge wells are the only failures and the reference is off
Escalate to the study director after a second failure on the same test lot
Brindlewythe Biosciences Ltd | Confidential 5

## Slide 6: Plate acceptance checklist
Check | Accept if | If not
Positive control | Inside the window across all duplicates | Rerun the plate
Negative control | Low signal, no edge effect | Rerun; check the reagent lot
Reference dose response | On its curve, same potency range as the last set | Rerun; tell the assay quality coordinator
Plate order drift | No step change between plates | Hold the set; check the lot record
Run sheet entry | Acceptance signed and dated | Do not release the plate
Brindlewythe Biosciences Ltd | Confidential 6

## Slide 7: Rerun rules
One rerun per plate with the same compound plate
A second failure goes to the study director with the run sheet attached
  Do not mix a rerun plate into the original set without a note
Excluded plates stay on the record with the reason
Brindlewythe Biosciences Ltd | Confidential 7
Notes: Still unclear whether the one-rerun rule applies to the hepatocyte plates. Ask Anika before the course.

## Slide 8: Reporting the screen gate
Acceptance is reported before the potency data
The screen gate decision is separate from any mechanism
  Say which plates were rerun and why
Potency figures go in the biology memo, not on the plate slide
Brindlewythe Biosciences Ltd | Confidential 8

## Slide 9: Open points for the next revision
Confirm the drift check frequency with the assay quality coordinator
Add the reagent lot field to the run sheet template
Decide who signs acceptance when the study director is away
Brindlewythe Biosciences Ltd | Confidential 9
Notes: Not for circulation. Mostly for me and Ines before the next round.