## Slide 1: Plate acceptance: training reference
Westravelle Analytical Ltd, a Tarnovell company | QA training | Reference copy, September 2024

## Slide 2: 1 Purpose
Plate acceptance decides whether a screening plate can be used for reporting at all
It is checked before any compound well is read
It is separate from system suitability, which applies to the chromatographic runs in the stability programme
  Both are recorded on the batch card; neither replaces the other
Westravelle Analytical Ltd, a Tarnovell company | Confidential 2
Notes: Trainees often confuse the two. Walk through the difference on slide 5 before they start on the bench.

## Slide 3: 2 Plate acceptance checks
Check | What is looked at | Action if it fails
Control wells present | Each control type is in the positions set in the plate map | Do not read; raise a deviation note
Positive control signal | Signal sits inside the window set in the protocol | Do not read; repeat the plate once
Negative control signal | Background is low and flat across the plate | Check reagent make-up and washing before any repeat
Edge wells | No drift from the outer rows and columns that is wider than the protocol allows | Note on the batch card; read only if the protocol permits
Z' for the plate | Calculated from the control wells as stated in the protocol | Plate rejected; no partial reporting
Westravelle Analytical Ltd, a Tarnovell company | Confidential 3
Notes: The window values live in the current protocol, not in this deck. Quote the protocol revision on the batch card.

## Slide 4: 3 Controls and layout
Controls go in the positions shown on the plate map
Do not move a control to rescue a plate
Plate map is printed and filed with the batch card
Replicate wells follow the layout in the protocol
Edge effects are looked at on every plate, not just new ones
Column 1 and 24 are used for controls only where the protocol says so
A plate with a missing control is not partly read
Westravelle Analytical Ltd, a Tarnovell company | Confidential 4

## Slide 5: 4 Failed plates
A failed plate is marked on the batch card and not deleted
Raise a deviation note for every rejected plate, giving the plate ID and the check that failed
One repeat is allowed where the protocol allows it; the repeat is recorded as a new plate
Two failures on the same compound set go to the QC method validation lead before any further work
Westravelle Analytical Ltd, a Tarnovell company | Confidential 5
Notes: Do not average the rejected plate into the repeat. Keep both on file.

## Slide 6: 5 Plate acceptance and system suitability
Plate acceptance is applied to each screening plate before reading
System suitability is applied to each chromatographic sequence before sample results are released
A passing plate does not show that the instrument was suitable on the day, and a passing sequence does not accept a plate
  Sequence sheets carry the system suitability entries; plate maps carry the plate acceptance entries
Both are signed by the analyst and checked by a second person before the batch card is closed
Westravelle Analytical Ltd, a Tarnovell company | Confidential 6
Notes: Saira Mahmood and Mark Campbell have agreed the wording of this slide. Check the current version of the protocol before use.