## Slide 1: Pull handover and system suitability
Westravelle Analytical Ltd, a Tarnovell company | Rev04 | 11 Apr 2025
Notes: Use the current protocol and method alongside this training. This deck defines the handover decisions; it does not create new pull windows or method limits.

## Slide 2: 1. Before a Stability pull
Leon Wu confirms the protocol, stability lot, condition and scheduled interval.
Check the chamber location and batch card before removing material.
Record actual removal date and time, chamber condition in °C and any storage excursion.
Use the approved pull window; escalate a missed window instead of backdating the pull.
Westravelle Analytical Ltd, a Tarnovell company | Confidential 2
Notes: The ICH chamber programme is tied to a condition and an interval. Similar container appearance does not justify substituting another stability lot. Retain the actual event history if the planned pull cannot proceed.

## Slide 3: 2. Handover is a reconciliation
Match container labels to the batch card and pull instruction.
Record units removed, retained, transferred and consumed.
Identify storage conditions and the destination of every transfer.
Denis Miller reconciles receipt against the handover record.
Resolve a missing, damaged or mismatched container before preparation.
Both sides record the handover; do not rely on an unlogged verbal exchange.
Westravelle Analytical Ltd, a Tarnovell company | Confidential 3
Notes: Do not convert a discrepancy into an assumed count. Keep the stability lot, condition and interval together through aliquoting. Actual quantities belong in the record; this training does not prescribe a universal pull quantity.

## Slide 4: 3. Minimum handover record
Record field | Required link | Stop and escalate when
Identity | Protocol; stability lot; batch card | Label and instruction disagree
Storage | Condition; interval; chamber location | Excursion or location is unresolved
Quantity | Removed; transferred; retained; consumed | Reconciliation is incomplete
Handling | Removal time; transport; receipt; interim storage | Required history is missing
Analysis | Method; sequence sheet; analyst | Preparation cannot be linked to the pull
Westravelle Analytical Ltd, a Tarnovell company | Confidential 4
Notes: A completed form is useful only if the links are correct. Record any discrepancy factually and preserve the original handover entries.

## Slide 5: 4. Percent label claim is not area percent
Assay: report as percent label claim.
Reference-standard basis, preparation and dilution support the assay calculation.
The denominator is the stated label claim, with the method-defined corrections.
Related substances: report as area percent where the method specifies it.
Peak integration and method-defined response treatment support the impurity result.
Area percent does not automatically equal mass percent or percent label claim.
Westravelle Analytical Ltd, a Tarnovell company | Confidential 5
Notes: Ask the trainee to identify the denominator before interpreting a value. Do not subtract impurity area percent from assay percent label claim to create an invented mass balance. Each endpoint uses its authorized calculation.

## Slide 6: 5. System suitability comes first
Saira Mahmood confirms the method-specific suitability criteria.
Sequence sheets identify standards, blanks, suitability injections and sample preparations.
Assess the required suitability responses before interpreting stability samples.
Check continuing suitability where the method requires it; an acceptable start does not guarantee the whole sequence.
Westravelle Analytical Ltd, a Tarnovell company | Confidential 6
Notes: Criteria belong to the approved HPLC method qualification or Assay and related-substances validation documentation. Do not invent common numerical thresholds across methods. Preserve chromatograms and integration history.

## Slide 7: 6. When suitability fails
Hold affected sample interpretation and client conclusions.
Record the failed criterion, sequence position and potentially affected samples.
Notify Saira Mahmood and Valerie Turner; open a factual deviation note.
Investigate preparation, instrument response and sequence events before deciding on repeat work.
Retain the original sequence and document the rationale for any reinjection or fresh preparation.
Westravelle Analytical Ltd, a Tarnovell company | Confidential 7
Notes: A later passing injection does not erase the earlier failure. Define the affected interval and what the investigation supports. Avoid selecting only a passing repeat without resolving the cause and reportability.

## Slide 8: 7. Release gate and client interpretation
Confirm identity and quantity reconciliation are complete.
Confirm system suitability and calculation review for each reported endpoint.
Assess deviations and storage excursions with their effect on interpretation.
Keep conclusions within the tested condition and interval.
Alice Penrose resolves scientific reporting questions; QA records the release decision.
Westravelle Analytical Ltd, a Tarnovell company | Confidential 8
Notes: Do not infer shelf life from an isolated pull or claim that an untested storage condition is supported. A report may state a limitation or pending investigation; commercial urgency does not change suitability requirements.

## Slide 9: 8. Handover exercise: make the next decision
A label differs from the pull instruction: hold preparation and reconcile the batch card.
A related-substances result is described as percent label claim: correct the endpoint and calculation basis before release.
Suitability fails after samples begin: define the affected sequence interval and escalate.
A client asks for a later interval: state what has been tested and scope the next pull.
Westravelle Analytical Ltd, a Tarnovell company | Confidential 9
Notes: Ask each trainee which record they would preserve and who they would contact. Valerie Turner records training completion in the local quality records. Rev04 is final as of 11 Apr 2025.