## Slide 1: Copy of Matrix Acceptance
Panel workflow training | Merrivoss annotations 05/12/2021 | Helen Marchwood Merrivoss Bioanalysis Inc, a Tarnovell company

## Slide 2: Panel workflow: acceptance belongs to the run
Confirm plate identity and assay worksheet before reviewing activity.
Read blanks and reference responses in context.
Flag an unsuitable run before interpreting article rankings.
Merrivoss Bioanalysis Inc, a Tarnovell company | Confidential 2
Notes: Original panel teaching sequence retained. Merrivoss annotation: preserve accession-lot identity when results cross between assays.

## Slide 3: Panel workflow | retained diagram
Merrivoss Bioanalysis Inc, a Tarnovell company | Confidential 3
Notes: Retained shared panel diagram. Merrivoss addition: tandem-MS analytical acceptance precedes use of concentrations for exposure conclusions.

## Slide 4: Local annotation: two acceptance questions
Accession lot: which material was received and used?
Preserve label, identity trail and handling notes.
An accession lot can appear in multiple runs.
Tandem-MS analytical batch: is this measurement sequence suitable?
Review calibration, matrix controls and qualifications.
Run acceptance does not establish material identity.
Merrivoss Bioanalysis Inc, a Tarnovell company | Confidential 4
Notes: The original panel language refers to run acceptance. Analytical batch here means a measurement sequence, not an accession lot.

## Slide 5: Before the run: keep the matrix visible
Record species and matrix on the assay worksheet.
Use appropriate matrix for calibration and reference checks.
An unchanged analyte name does not establish method transfer.
Merrivoss annotation: attach matrix context to the analyte card.
Merrivoss Bioanalysis Inc, a Tarnovell company | Confidential 5

## Slide 6: Reference checks: compare like with like
Review reference response within the method and matrix in use.
Investigate blank response, carryover and unexpected background.
Historical response is context, not a limit unless the procedure defines it.
Keep the original observation when a qualified rerun is needed.
Merrivoss Bioanalysis Inc, a Tarnovell company | Confidential 6

## Slide 7: Panel record to tandem-MS record
Retained panel element | Merrivoss annotation
Plate map | Link to article and accession lot
Blank and reference checks | Retain matrix-specific evidence
Run acceptance | Assess analytical batch separately
Article interpretation | Resolve identity before release
Report review | Carry limits into the DMPK memo
Merrivoss Bioanalysis Inc, a Tarnovell company | Confidential 7
Notes: Training crosswalk, not a change to a validated procedure.

## Slide 8: Reporting limits: avoid a false zero
Below quantitation means no reportable concentration can be assigned.
It does not demonstrate absence of analyte.
Preserve qualifications through concentration summaries and exposure calculations.
Merrivoss annotation: state the handling rule before the exposure conclusion.
Merrivoss Bioanalysis Inc, a Tarnovell company | Confidential 8

## Slide 9: Discussion exercise: identity and response
The reference response is suitable, but a vial label disagrees with the assay worksheet.
Would run acceptance resolve the label discrepancy?
Hold named-article interpretation until the identity trail is resolved.
Record the action in the analyte card rather than silently changing the name.
Merrivoss Bioanalysis Inc, a Tarnovell company | Confidential 9
Notes: Qualitative classroom scenario; no client study or numerical result is implied.

## Slide 10: Closeout checklist | Helen Marchwood
Retain the panel workflow diagram when reusing this copy.
Use accession lot for material tracking and analytical batch for tandem-MS acceptance.
Escalate identity or matrix questions before the exposure gate.
Attach acceptance decisions and qualifications to the assay worksheet.
Merrivoss Bioanalysis Inc, a Tarnovell company | Confidential 10
Notes: Final training copy, 05/12/2021. Local annotations supplement the shared panel workflow; study-specific procedures govern acceptance.